## Slide 2: Previous Minutes of Meeting
Build a stable “Follow AprilTag” Program.
Combine manual control (WASD) along with AprilTag detection.
An user interface for specific tasks.
Integrate Ricoh Theta as a payload device.
Reduce lagging and camera errors.

## Slide 3: Progress
Implemented AprilTag detection with multiple fisheye cameras.
Implemented rotational scanning if tag is lost.
Added manual WASD control alongside menu actions, so we can use autonomous commands as well.
Fixed multiple camera errors and prevented crashes by converting RAW frames to grayscale frames (8-bit), which reduced the processing load on core.
Ricoh Theta camera live feed connection without Core I/O.

## Slide 4
SPOT (Via SPOT network)
Laptop
Ricoh Theta
Ricoh Theta Communication

## Slide 5: Next Goals
Improve searching ability of SPOT
Improve on Tag Following behaviour
Combining Xbox controller with current program
Combine Ricoh Theta with current program